## Slide 1: Logic Instructions
Course Code: 0052
Dept. of Computer Science
Faculty of Science and Technology
Lecturer No: | 7(a) | Week No: | 9 | Semester: | Summer 21-22
Lecturer: | Dr. Md Mehedi Hasan; mmhasan@aiub.edu |  |  |  | 
Course Title: : Computer Organization and Architecture

## Slide 2: Overview : LOGIC
Instructions to change the bit pattern in a byte or word
The ability to manipulate bits manually which is unlikely in high level languages (Except C)
Logic Instructions: AND, OR, XOR and NOT
Logic Instructions can be used to clear, set, and examine bits, a register or variable. i.e. these will be used for
    Converting a lowercase letter to upper case
      Determining If a register contains an even or odd number.

## Slide 3: Overview: SHIFT
Bits can be shifted left or right in a register or memory location.
When a bit is shifted out, it goes into CF.
Because a left shift doubles a number and a right shift halves it, these instructions give us a way to multiply and divide powers of 2.
Shifting is much faster than Multiplication and Division.

## Slide 4: LOGIC Instructions
The ability to manipulate individual bits is one the main advantages of assembly language.
Individual bits can be changed in computer by using logic operations.
The binary values of 0 = False and 1= True
When a logic operation is applied to 8- or 16-bit operands, the result is obtained by applying the logic operation at each bit position.

## Slide 5: Truth Table for AND, OR, XOR and NOT

## Slide 6: Solve the Following
AND Operation: 10101010 AND 11110000
OR Operation: 10101010 OR 11110000
XOR Operation: 10101010 XOR 11110000
NOT Operation: NOT 10101010

## Slide 7: Solution
10101010
AND 11110000
=10100000
10101010
OR 11110000
=11111010
10101010
XOR 11110000
= 01011010
NOT 10101010
=01010101
3
1
2
4

## Slide 8: AND, OR, and XOR instructions
The AND, OR, and XOR instructions perform the named logic operations. The formats are:
The result of the operation is stored in the destination, which must be a register or memory location.
The source may be a constant, register, or memory location.
However, memory-to-memory operations are not allowed.
    AND destination, source
    OR destination, source
    XOR destination, source

## Slide 9: Effect on Flags
  SF, ZF, PF reflect the result
  AF is undefined
  CF, OF= 0
One use of AND, OR, and XOR is to selectively modify the bits in the destination.
To do this, we construct a source bit pattern known as mask.
The mask bits are chosen so that the corresponding destination bits are modified in the desired manner when the instruction is executed.

## Slide 10: MASK
To choose the mask bits, we make use of the following properties of AND, OR, and XOR:
b AND 1 = b
b OR 0 = b
b XOR 0 = b
b AND 0 =0
b OR 1 = 1
b XOR 1 = ~b (complement of b)

## Slide 11
The AND instruction can be used to CLEAR specific destination bits while preserving the others.
  A 0 mask bit clears the corresponding destination bit.
  a 1 mask bit preserves the corresponding destination bit.
The OR instruction can be used to SET specific destination bits while preserving the others.
  A 1 mask bit sets the corresponding destination bit.
  A 0 mask bit preserves the corresponding destination bit. ·
The XOR instruction can be used to complement specific destination bits while preserving the others.
  A 1 mask bit complements the corresponding destination bit;
  A 0 mask bit preserves the corresponding destination bit.

## Slide 12: Clear bit
Example
Clear the sign bit of AL while leaving the other bits unchanged
Solution:
  Use the AND instruction with 0111 1111b=7Fh as the mask.
  Thus. AND AL,7Fh

## Slide 13: Clear bit
Example
AND Instruction:The AND instruction is a bitwise logical AND operation.It works by comparing each corresponding bit of the destination (AL) and the mask (7Fh) and following these rules:0 AND any value = 0 (clears the bit)1 AND any value = that value (preserves the bit)

## Slide 14: Clear bit
Example
Step-by-Step Solution:
We want to clear only the sign bit (b7) of AL, so it must become 0.
All other bits (b6 to b0) should remain unchanged.
We use a mask of 0111 1111b, which is 7Fh in hexadecimal.
  This mask has 0 at the b7 position (the sign bit), which will clear it.
  All other bits are 1, so they will preserve the corresponding bits in AL.
The instruction used is:
AND AL, 7Fh

## Slide 15: Clear bit
Example
1001 1010 (AL value)
AND 0111 1111 (Mask 7Fh)
------------------
0001 1010
Result: 0001 1010b (1Ah in hexadecimal).The sign bit (b7) is cleared, while all other bits remain unchanged.

## Slide 16: Set or Complement Bit
Example: Set the most significant and least significant bits of AL while preserving the other bits.
  Solution: Use the OR instruction with 1000 0001b =81h as the mask.
  Thus, OR AL,81h
Example: Change the sign bit of DX.
  Solution: Use the XOR instruction with a mask of 8000h.
  Thus, XOR DX,8000h
*** To avoid typing errors, it's best to express the mask in hex rather than binary, especially if the mask would be 16 bits long.

## Slide 17: Converting an ASCII Digit to a Number
when program reads a character or digit from the keyboard, AL gets the ASCII code of the character.
For example, if the "5" key is pressed, AL gets 35h instead of 5. To get 5 in AL, we did
    SUB AL,30h
We can also do this by using an AND instructions to clear the high four bits of AL.
    AND AL,0Fh
As the ASCII codes of "0" to "9" are 30h to 39h, this method will convert any ASCII digit to a decimal value.
Using AND emphasizes on modifying bit pattern of AL and makes program more readable.
Problem: convert a stored decimal digit to Its ASCII code?

## Slide 18: Converting a Lowercase Letter to Upper Case
The ASCII codes range for
  "a" to “z" is 61h to 7Ah
  "A" to "Z" is 41h to 5Ah.
So, to convert a lowercase to UPPERCASE we use the following operation:
  Sub DL,20h
However, if we compare binary codes of corresponding lower and uppercase letters,

## Slide 19: Converting a Lowercase Letter to Upper Case
The ASCII codes range for
  "a" to “z" is 61h to 7Ah
  "A" to "Z" is 41h to 5Ah.
ASCII Code and Bit Representation:
ASCII codes for lowercase letters ('a' to 'z') range from 61h (0110 0001b) to 7Ah (0111 1010b).
ASCII codes for uppercase letters ('A' to 'Z') range from 41h (0100 0001b) to 5Ah (0101 1010b).

## Slide 20: Conversion using AND
To convert lower to upper case we need to clear only bit 5. This can be done by using an AND instruction with the mask 11011111 or 0DFh. So if the lowercase character to be converted is In DL, we execute
AND DL, 0DFh

## Slide 21: Clearing a Register
MOV AX,0
SUB AX,AX
XOR AX,AX [1 XOR 1 = 0 and 0 XOR 0=0]
Testing a Register for Zero
To test the contents of a register for zero, or to check the sign of the contents, we may use:
CMP CX,0

## Slide 22: Not Instruction
The NOT instruction performs the one's complement operation on the destination. The format is:
  NOT destination (**No effect on status flags)
  Example: Complement the bits in AX:
      NOT AX

## Slide 23: TEST Instruction
The TEST Instruction performs an AND operation of the destination with the source but does not change the destination contents.
The purpose of the test instruction is to set the status flags. The format is:
    TEST destination, Source
Effects of flags on test operation:
  CF, OF =0
  AF = Undefined
  SF, ZF, PF reflect the result

## Slide 24: Bit Examination on TEST
TEST instruction can be used to examine individual bits in operand.
The mask should contain 1's in the bit positions to be tested and 0’s elsewhere
    As 1 AND b = b, 0 AND b = 0
The operation TEST destination, mask
Will have 1's in the tested bit positions if and only if the destination has 1’s in these positions; and 0’s elsewhere.
if the destination has 0’s in all the tested positions, the result will be 0 and thus ZF=1

## Slide 25: Find Even Number
Example: Jump to label BELOW If AL contains an even number.
Solution: Even numbers have a 0 in bit 0. Thus, the mask is 00000001b=1
      TEST AL, 1
      JZ BELOW

## Slide 26
The shift and rotate instructions shift the bits in the destination operand by one or more positions either to the left or right.
For a shift instruction, the bits shifted out are lost
For a rotate instruction, bits shifted out from one end of the operand are put back into the other end.
The instruction have two possible formats. For a single shift or rotate, the form is
    Opcode destination,1
For a shift or rotate of N positions, the form is
    Opcode destination, CL
Where CL contains N In both cases, destination is an 8- or 16-bit register or memory location.

## Slide 27: Shift Instructions…
Shift or Rotate instructions can be used to multiply and divide by powers of 2, and we will use them in programs for binary and hex I/O
***Note that for Intel's more advanced processors, a shift or rotate instruction also allows the use of an 8-bit constant.

## Slide 28: Left Shift (SHL) Instructions
The SHL (shift left) instruction shifts the bits in the destination to the left. The format for a single shift is
      SHL destination, 1
A 0 is shifted into the rightmost bit position and the msb is shifted into CF. If the shift count N is different from 1, the instruction takes the form
  SHL destination, CL (Here CL contains N and the above instruction made N single shifts)
    The value of CL remains the same after the shift operation

## Slide 29: SHL Instruction
Example: Suppose DH contains 8Ah and CL contains 3. What are the values of DH and of CF after the instruction SHL DH,CL is executed?
The binary value of DH is 1000 1010. After 3 left shifts, CF will contain 0. The new contents of DH may be obtained by
Erasing the leftmost three bits
Adding three zero bits to the right end, thus 01010000b = 50h.

## Slide 30: Left Shift (SHL) Instructions
SHL Operation Example
Initial Values:
CL = 3 (Number of positions to shift left)
Instruction: SHL DH, CL
DH = 8Ah (Binary: 1000 1010)
Step-by-Step Calculation
Initial Binary Value of DH:
1000 1010 (Binary for 8Ah)
Shifting Left by 3 Positions:
  After First Shift:
0001 0100 (The bit '1' that is shifted out is saved in CF) CF = 1
  After Second Shift:
0010 1000 (The bit '0' is shifted out) CF = 0
  After Third Shift:
0101 0000 (The bit '0' is shifted out) CF = 0
Final Results
Final Value of DH = 50h (Binary: 01010000)
Final Value of CF = 0

## Slide 31: Left Shift (SHL) Instructions
The Carry Flag (CF) in a shift operation (SHL) captures the last bit that is shifted out of the register.For each shift left, the leftmost bit is removed (shifted out), and a new bit (0) is introduced on the right.If the bit that is shifted out is 1, then CF = 1.If the bit that is shifted out is 0, then CF = 0.

## Slide 32: Multiplication by Left Shift
Let us consider a decimal number 235.
  If each digit is shifted left and 0 is attached on the right end, we get 2350 which is same as multiplying by 10.
  Similarly, a left shift on a binary number multiplies it by 2.
For example, suppose that AL contains 5=0000 0101b
  A left shift gives 0000 1010b = 10 thus doubling its value.
  Another left shift yields 0001 0100= 20d, so it is doubled again.

## Slide 33: Shift Arithmetic Left (SAL)
SHL Instruction can be used to multiply an operand by multiples of 2.
However, to emphasize the arithmetic nature of the operation the opcode SAL (shift arithmetic left)often used in instances for numeric multiplication.
Both instructions generate the same machine code.
When we treat left shifts as multiplication, overflow may occur.
For a single left shift, CF and OF accurately indicate unsigned and signed over- flow, respectively.
However, the overflow flags are not reliable indicators for a multiple left shift as multiple shift is really a series of single shifts, and OF and CF only reflect the result of the last shift.

## Slide 34: Right Shift (SHL) Instructions
The instruction SHR (shift right) performs right shifts on the destination operand
        SHR destination, 1
A 0 is shifted Into the msb position, and the rightmost bit is shifted
        SHR destination, CL
        ** here CL contains N In this case N single right shifts are made. The effect on the flags is the same as for SHL

## Slide 35
References
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
http://faculty.cs.niu.edu/~byrnes/csci360/notes/360shift.htm

## Slide 36
Books
Assembly Language Programming and Organization of the IBM PC, Ytha Yu and Charles Marut, McGraw Hill, 1992. (ISBN: 0-07-072692-2).
Essentials of Computer Organization and Architecture, (Third Edition), Linda Null and Julia Lobur
W. Stallings, “Computer Organization and Architecture: Designing for performance”, 67h Edition, Prentice Hall of India, 2003, ISBN 81 – 203 – 2962 – 7
Computer Organization and Architecture by John P. Haynes.