## Slide 1
Electronic Devices
Reference book:
Electronic Devices and Circuit Theory (Chapter-2)
Robert L. Boylestad and L. Nashelsky , (11th Edition)
Mid Term Lecture - 05
Faculty Name: Dr. Md. Kabiruzzaman
Email : kabiruzzaman@aiub.edu

## Slide 2: Objectives
Be able to predict the output response of a clipper and clamper diode configuration.

## Slide 3
Clippers are networks that employ diodes to “clip” away a portion of an input signal without distorting the remaining part of the applied waveform.
The half-wave rectifier is an example of the simplest form of diode clipper- one resistor and a diode. Depending on the orientation of the diode, the positive or negative region of the applied signal is “clipped” off.
There are two general categories of clippers: series and parallel.
The series configuration is defined as one where the diode is in series with the load, whereas the parallel variety has the diode in a branch parallel to the load.
CLIPPERS

## Slide 4: CLIPPERS: SERIES
Diode is in series with the load.

## Slide 5: Series Clipper with a dc supply

## Slide 6: CLIPPERS: SERIES
Use transition voltage to define “on” and “off” regions
Draw the output waveform directly below the applied voltage using the same scales for the horizontal axis and the vertical axis.
Negative half cycle clipped away in output waveform

## Slide 7: CLIPPERS: SERIES
Determine transition level

## Slide 8: CLIPPERS: SERIES
For vi = 20 V (0 --> T/2) the network results,
The diode is in the short-circuit state.
vo = 20V + 5V = 25V

## Slide 9
For vi = -10 V (T/2 --> T) the network results,
The diode is in the “off” state.
vo = iRR = (0)R = 0 V
The resulting output voltage corresponds to input voltage appears as:

## Slide 10: CLIPPERS: PARALLEL
Diode in a branch parallel to the load.

## Slide 11: CLIPPERS: PARALLEL
Determine output across the series combination of the diode and the 4-V supply
Determine transition level of input voltage.
Condition:
Replace circuit with short-circuit equivalent.
Diode current is 0 mA.

## Slide 12
For , diode is on.
For , diode is off.

## Slide 13: CLIPPERS: PARALLEL
Si
Determine transition level of input voltage.
Condition:
Replace circuit with diode equivalent circuit.
Diode current is 0 mA.
Applying KVL around output loop in clockwise direction,

## Slide 14
For , ID direction is counter-clockwise.
Diode is off.
For , ID direction is counter-clockwise
Diode is on.

## Slide 15: CLIPPERS
Simple Series clippers (Ideal Diodes) for the sinusoidal input
Biased Series Clippers (Ideal Diodes)

## Slide 16: CLIPPERS
Simple Parallel clippers (Ideal Diodes) for the sinusoidal input
Biased Parallel Clippers (Ideal Diodes)

## Slide 17: CLAMPERS
A clamper is a network constructed of a diode, a resistor, and a capacitor that shifts a waveform to a different dc level without changing the appearance of the applied signal.
The output signal is clamped to 0 V for the interval 0 to T/2 but maintains the same total swing (2V ) as the input.

## Slide 18
Step 1: Start the analysis by examining the response of the portion of the input signal that will forward bias the diode.
Step 2: During the period that the diode is in the “on” state, assume that the capacitor will charge up instantaneously to a voltage level determined by the surrounding network.
Step 3: Assume that during the period when the diode is in the “off” state the capacitor holds on to its established voltage level.
For the interval 0 -> T/2 :
For the interval T/2 -> T :
CLAMPERS

## Slide 19
Step 4: Throughout the analysis, maintain a continual awareness of the location and defined polarity for vo to ensure that the proper levels are obtained.
Step 5: Check that the total swing of the output matches that of the input.
The output signal maintains the same total swing (2V) as the input.

## Slide 20: CLAMPERS
From t1 to t2 period of the input signal the diode will be forward biased.

## Slide 21
From t2 to t3 period of the input signal the diode will be reverse biased
The output swing of 30 V matches the input swing.
See Example 2.23

## Slide 22: Clamping Networks

## Slide 23
Thank You